## Slide 2: Upgrades to the Horizon Simulation Framework
Brian Butler – L-3 Communications
Eric Mehiel – Cal Poly, San Luis Obispo

## Slide 3: Presentation Overview
What is the Horizon Simulation Framework (HSF)?
Version History (1.0 – 2.1 )
Upgrades to Version 2.2
  Dynamic Model Creation
  Lua Scripting Support
  Multi-threaded Processor Support
Performance Test Results
Conclusions and the Future of the HSF

## Slide 4: What problem is HSF trying to solve?
"Systems Engineering Process II" by Leon Osborne, Jeffrey Brummond, Robert Hart, Mohsen (Moe) Zarean Ph.D., P.E, Steven Conger https://commons.wikimedia.org/wiki/File:Systems_Engineering_Process_II.svg#/media/File:Systems_Engineering_Process_II.svg
Verification and Validation of System Level Requirements can be difficult if the system is not operations
Notes: Main system level requirements can best be verified by simulation (Utility or Use Requirements)
Attack the problem by developing a model of the system that, when exercised, will simulate the behavior of the system over time

## Slide 5: How is HSF structured?
Notes: A state transition function coupled with a scheduling algorithm
Modeling Component
  Input = state of system at t0 (state0)
  Output = state of system at t1 (state1)
  Architecture = a System comprised of subsystems
Scheduling Component
  If the process of going from state0 to state1 does not violate any system constraints, the change in the state is scheduled as an event
  To find the “best” schedule, the scheduler tries “all” possibilities

## Slide 6: Modeling Relationships In HSF
SubsystemNode 1
SubsystemNode 6
SubsystemNode 2
SubsystemNode 3
SubsystemNode 9
SubsystemNode 8
SubsystemNode 10
SubsystemNode 12
SubsystemNode 11
SubsystemNode 7
SubsystemNode 5
SubsystemNode 4
Asset 3
Asset 1
Asset 2
Notes: Constraints – a limit on values of a system state variable
Dependency – describes the relationship between one or more subsystems
Asset – a collection of subsystems with some significant meaning to the modeling engineer

## Slide 7: HSF Output
Event
Event
Event
Event
Event
Event
Initial State
Initial State
Asset Schedule 1
Asset Schedule n
System Schedule
Simulation Time
A full description of the state of all subsystems and assets of the system
Notes:   A full state description of the system over a user specified time frame (a schedule)

## Slide 8: Example of using HSF
Aeolus: The Greek ruler of wind
Extreme-weather imaging satellite
Circular, 1000km, 35 degree inclined orbit
Simulation date: August 1st 2008 for 3 revolutions
Targets clustered into high-risk areas, including Southeast Asia and the Gulf of Mexico
Sensor has ability to generate data while in eclipse
A day-in-the-life of the Aeolus constellation
Notes:   Aeolus Test Case – Rev. In The Life used to verify a utility based system-level requirement

## Slide 9: The Aeolus Results: Visualization
Matlab visualization of HSF simulation results

## Slide 10: The Aeolus Results: Rev. In The Life Data

## Slide 11: HSF version history
1.0 – Initial Release
1.1 – Math Libraries Added
1.2 – State Profile Added
2.0 – Multi-Asset Capability
2.1 – Auto Circular Dependency Check
All open source in C++

## Slide 12: HSF Functional Overview @ v2.1
Scheduler/System Interface
Main Scheduling Algorithm
System Parameters (Custom Model File)
Simulation Parameters (Custom Simulation File)
Final Schedule, State Data (Output)
System Model
Subsystem
Subsystem
Subsystem
Horizon Simulation Framework
Interface between Subsystems
Task Inputs
(Custom Task File)
Modeling Utilities
Code Interactions
Input/Output Interfaces

## Slide 13: Upgrade: Dynamic Model Creation
<MODEL>
<ASSET>
<SUBSYSTEM
Type=“scripted”
Name=“Sub 1”
SubId=”1”
</SUBSYSTEM>
<SUBSYSTEM
Type=“Sub 2”
SubId=”2”
<DEPENDENCY SubId="2"></DEPENDENCY>
</SUBSYSTEM>
</ASSET>
<ASSET>
<SUBSYSTEM
Type=“scripted”
Name=“Sub 3”
SubId=”3”
<DEPENDENCY SubId="2"></DEPENDENCY>
<DEPENDENCY SubId="4"></DEPENDENCY>
</SUBSYSTEM>
<SUBSYSTEM
Type=“Networked”
Name=”Sub 4”
host=”127.0.0.1”
port=”9999”
SubId=”4”
</SUBSYSTEM>
</ASSET>
</MODEL>
Subsystem “Sub1”
SubId: 1
Type: Scripted
Asset 1
Asset 2
Subsystem “Sub 2”
SubId: 2
Type: Compiled
Subsystem “Sub 4”
SubId: 4
Type: Networked
Host: 127.0.0.1
Port: 9999
Subsystem “Sub 3”
SubId: 3
Type: Scripted
Notes: Problem: The form of the model was hard coded into the main() function
Solution: Use xml data files
Result: More flexibility in the types and functionality of system models

## Slide 14: Dynamic Model Creation Detail
In version 2.1 only several (hard coded) subsystems were available to the user without modification to the codebase
Using an input file in xml format, the type of each subsystem and the structure of the system model is contained in the input file
Adding scripting also increased the flexibility of HSF by easily allowing customizable subsystem models (more next)

## Slide 15: Upgrade: Lua Scripting Support
System Model
Subsystem
Subsystem
EOMS
Main Scheduling Algorithm
Schedule
Evaluator
Subsystem
Subsystem
Subsystem
Subsystem
Notes: Problem: Many classes within HSF required manual modification and recompilation when functionality or variable types were changed or added
Solution: Add scripting support to different parts of the HSF to increase flexibility and eliminate user required code changes
Result: A more flexible and tightly integrate simulation tool

## Slide 16: Lua Scripting Support Detail
Lua is a scripting language used in many C/C++ applications
A Lua Binding library allows the developer to bind Lua script calls to C/C++ function calls
The Lua scripts are then interpreted at run-time and the associated C/C++ functions are called

## Slide 17: Lua Scripting Points
Lua Scripting was added to the follow components to increase the flexibility of the HSF
Subsystems
  Initialization
  canPerform
  canExtend
Dependencies
Schedule Evaluator
Equations of Motion (EOMS)

## Slide 18: Upgrade: Multi-Threading Support
Assign at most N schedules to threads
Have the last schedule been assigned to a thread?
Wait for a thread to finish
Set schedule pass/fail state
Assign new schedule to a thread
Set pass/fail state for all remaining schedules
Done!
Notes: Problem: The baseline scheduling algorithm is formulated as “an embarrassingly parallel” problem
Solution: Add multi-threading at the highest level of the scheduling algorithm
Result: Improved performance with very little multi-threading overhead

## Slide 19: Multi-Threading Support Detail
Since each proposed schedule is independent (lives in another universe) pass each new proposed schedule off to the next available thread for processing

## Slide 20: HSF Functional Overview @ v2.2
Scheduler/System Interface
Main Scheduling Algorithm
System Parameters (Model XML File)
Simulation Parameters (Simulation XML File)
Final Schedule, State Data (Output)
System Model
Subsystem
Subsystem
Subsystem
Horizon Simulation Framework
Interface between Subsystems
Lua Scripts (Input)
Task Inputs
(Task XML File)
Modeling Utilities
Scripting Utilities
Code Interactions
Input/Output Interfaces
Multi-Threading Support

## Slide 21: Lua Scripting Runtime Testing Results

## Slide 22: Multi-Threaded Runtime Results
Chart: Simulation Runtime (s)
| 100 | 500 | 1000 | 2000 | 5000 | 10000
Total Time (1 Thread) | 1.0025 | 0.99878 | 0.99975 | 1.0006 | 0.99996 | 0.9992
Total Time (2 Threads) | 0.65455 | 0.61378 | 0.60818 | 0.63605 | 0.57742 | 0.56501
Total Time (3 Threads) | 0.52602 | 0.46047 | 0.44875 | 0.49002 | 0.41804 | 0.40435
Total Time (4 Threads) | 0.46374 | 0.38533 | 0.36686 | 0.41442 | 0.3292 | 0.31556

## Slide 23: Conclusions and the Future of HSF
Three upgrades were made to HSF for v2.2
  Dynamics Model Creation
  Lua Scripting Support
  Multi-Threading Support
Current/Future Work
  Convert code base to C#/Python
  Gather information about why the system cannot perform a task
  Interplanetary model development